## Slide 1
SIH26054 · SMART INDIA HACKATHON 2026
DIGITAL TWIN FOR MALE UAV
AERO-PISTON ENGINE
Unified System Architecture — physics-informed AI for real-time engine health monitoring, fault prediction, and mission reliability
Physics Simulation
AI/ML Core
Real-Time Systems
Validation & Deliverables
Four research domains, merged into one buildable software system.
Team AETS · Problem Statement: AI-Enabled Real-Time Digital Twin System
for Health Monitoring, Fault Prediction & Mission Reliability Enhancement

## Slide 2
01 · THE CORE PRINCIPLE
From Reactive Alarms to a Trustworthy Predictive Twin
Not an LSTM project, and not a monitoring dashboard — a synchronized, physics-informed Digital Twin.
Reactive Monitoring
Fixed thresholds fire only after a value already crossed a limit
No sense of degradation building beforehand
Predictive Monitoring
Learns expected engine behaviour
Flags deviation before a severe threshold breach
Digital Twin (our target)
Continuously synchronizes telemetry, context, physics and AI
State estimation + prediction + decision support, together
What SIH26054 explicitly asks for:
State estimation
Anomaly detection
Fault prediction
Degradation tracking
RUL estimation
Mission simulation + replay
Core design principle: The AI is one intelligence layer inside the Twin — not the Twin itself. Physics defines expected behaviour; AI learns what physics alone can't capture; fusion produces the Twin's live state.
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 02

## Slide 3
02 · TEAM SYNTHESIS
Four Research Domains, Merged Into One System
Every member's research maps directly onto a required PS section and a working module — nothing collected is decorative.
1
Physics & Simulation
Causal engine physics: atmosphere -> airflow -> combustion -> torque -> thermal/oil -> vibration
8 fault types injected as physics changes, not sensor overrides
Delivers: simulator, datasets, physics residual baseline
2
AI/ML Core
State estimation (Kalman) + shared multi-task LSTM (forecast / anomaly / RUL)
Ensemble anomaly detection, particle-filter RUL, conformal uncertainty
Delivers: trained model, health/severity/RUL engine
3
Real-Time Systems & Dashboard
Common telemetry schema shared by simulator and real hardware
FastAPI + WebSocket streaming; CAN reserved for real engine link
Delivers: backend, storage schema, operator dashboard
4
Validation & Deliverables
Environmental-mode accuracy corrections (altitude, heat, endurance, throttle)
Detection-time / false-alarm test plan for all 8 faults
Delivers: validation report, demo script, documentation
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 03

## Slide 4
03 · FLAGSHIP SYSTEM ARCHITECTURE
The Complete Pipeline: Engine to Operator
Two interchangeable sources feed one common pipeline — replacing the simulator with real hardware never touches the Twin or dashboard.
REAL ENGINE PATH
Sensors -> ECU/FADEC -> CAN
PROTOTYPE PATH
Physics Simulator (Member 1)
>
EDGE GATEWAY
Validate + Normalize schema
>
STATE ESTIMATION
Kalman filter: physics + sensors -> best estimate
>
SHARED LSTM CORE
One encoder, 3 heads: forecast / anomaly / RUL
v
ENSEMBLE ANOMALY
Forecast residual + CUSUM change-point
>
PHM LAYER
Health index - Fault diagnosis - RUL (particle filter + conformal UQ)
>
STORAGE
PostgreSQL: telemetry + health + fault history
>
GCS DASHBOARD
WebSocket -> React: live health, alerts, replay
Design rule: the simulator and real engine emit the identical normalized telemetry schema — every downstream module is source-agnostic by construction.
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 04

## Slide 5
04 · MEMBER 1 · PHYSICS SIMULATION CORE
The Causal Physics Chain Behind Every Telemetry Point
Faults are built by changing physics parameters, never by writing directly to a sensor value.
ATMOSPHERE
P, rho vs altitude
>
AIRFLOW
m_a = rho*Vd*(RPM/120)*eta_v
>
FUEL + COMBUSTION
heat release, power
>
TORQUE + RPM
J dw/dt = T_eng - T_prop - T_fric
>
THERMAL + OIL
Cth dT/dt = Qgen - Qrej
>
VIBRATION
baseline + harmonics + fault
Fault injection -> modifies the physics parameters at any point in this chain (e.g. cooling health, injector health), and every downstream sensor reading changes as a consequence.
Inputs -> Hidden States -> Outputs
Inputs: altitude, ambient T/P, airspeed, throttle, mission phase
Hidden states: combustion / cooling / injector / lubrication health
Outputs: RPM, CHT, EGT, oil P/T, vibration, fuel flow
Physics Residuals — the Bridge to AI
r = measured - physics-predicted, at the same operating point
A growing residual under comparable load/altitude signals real degradation
AI trains on ground-truth health labels; inference sees only telemetry
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 05

## Slide 6
05 · FAULT LIBRARY
8 Fault Types — Causal, Multi-Sensor Signatures
Diagnosis uses evidence across correlated sensors, never a single-parameter threshold.
Fault Type | Root Physics Change | Multi-Sensor Signature
Misfire | Cylinder torque contribution drops | RPM irregularity ^, vibration ^, cylinder EGT deviation
Injector abnormality | Fuel delivered != commanded | Fuel flow error, EGT/CHT shift, torque imbalance
Cooling degradation | Heat rejection falls | CHT ^ (slow trend), oil temp ^, possible oil-pressure dip
Lubrication loss | Oil pressure / film breaks down | Oil pressure v, friction ^, oil temp ^, vibration ^
Combustion instability | Cycle-to-cycle variance rises | EGT variance ^, vibration ^, RPM oscillation
Overheating trend | Heat generated > rejected, sustained | CHT + EGT + oil temp rising together
Abnormal vibration | Mechanical / bearing irregularity | Vibration RMS and crest factor rise vs baseline
Sensor drift / failure | Measurement wrong, engine healthy | One sensor diverges while correlated signals stay normal
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 06

## Slide 7
06 · MEMBER 4 · MISSION SIMULATION
5 Environmental Modes, Validated Against Reality
Same engine, different operating context — each mode was checked against aviation reference sources, not assumed.
NORMAL
Stable baseline across all parameters
HIGH ALTITUDE
Manifold pressure falls; CHT/EGT trend up unless leaned
HOT WEATHER
Biggest riser of all modes — oil temp & CHT climb fastest
ENDURANCE
Slow thermal soak then plateau; watch trend, not value
RAPID THROTTLE
Manifold pressure reacts in ~1-2s; CHT/EGT lag by seconds
Parameter | Normal | High Altitude | Hot Weather | Endurance | Rapid Throttle
CHT | Steady mid-range | Trending up | Up — worst case | Slow drift, then flat | Lags throttle by seconds
Oil Pressure | Steady | Near stable | Slightly down | Slow decline = wear sign | Brief dip on change
Vibration | Low baseline | Little direct effect | Little direct effect | Slow creep = wear sign | Short transient spikes
Fuel Flow | Matches power map | Needs leaning | Similar, less dense air | Very stable signal | Near-instant response
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 07

## Slide 8
07 · MEMBER 3 · REAL-TIME DATA PIPELINE
One Common Interface, Two Interchangeable Sources
Real hardware and the prototype simulator both speak the same normalized telemetry schema.
REAL ENGINE
Sensors -> ECU/FADEC -> CAN/SocketCAN -> Edge Gateway
PROTOTYPE
Physics simulator -> identical telemetry interface
>
COMMON PIPELINE
Normalize -> Validate -> Digital Twin -> AI
>
OPERATOR
WebSocket push -> live dashboard state
CAN / SocketCAN
Used close to the engine: ECU/FADEC -> CAN -> Linux gateway
python-can decodes frames on the real-hardware path only
Judge answer: 'CAN is for engine/vehicle communication'
WebSocket
Used between backend and dashboard, not near the engine
Server pushes the latest processed state immediately — no polling
Judge answer: 'WebSocket is for real-time application-layer delivery'
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 08

## Slide 9
08 · MEMBER 2 · AI/ML CORE
State Estimation + Shared Multi-Task Forecasting
Kalman-filtered state feeds one shared encoder with three purpose-built heads.
PHYSICS MODEL
Expected state from Member 1's simulator
>
LIVE SENSORS
Real or simulated telemetry
>
KALMAN FILTER
Fuses physics + sensors into one best-estimate state
>
SHARED LSTM ENCODER
Forecast head / Anomaly head / RUL head
Why a Kalman filter
Standard aerospace state-estimation tool; fuses noisy sensors with a physics prediction
Directly answers the PS's named 'real-time state estimation' requirement
Every downstream computation runs on this cleaner estimate, not raw noise
Why one shared multi-task encoder
Forecast, anomaly and RUL heads trained jointly on one LSTM encoder
More parameter-efficient on limited synthetic/simulated data than 3 separate models
30-60 timestep window in, next-K states + severity + RUL out
Decision rule: keep the simplest model that provides a meaningful, validated improvement — benchmark LSTM against persistence and moving-average baselines before trusting it.
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 09

## Slide 10
09 · TRUST LAYER
Why a Judge Should Believe Our Alerts
Two detectors, calibrated uncertainty, and a sensor self-check — before any number reaches the operator.
Ensemble Anomaly
Detector 1: forecast-residual deviation — catches sharp deviations
Detector 2: CUSUM / Page-Hinkley change-point — catches slow drift
RUL — Particle Filter
Propagates the physics degradation model as weighted trajectories
Literature-standard for RUL with genuine uncertainty
Conformal Prediction
Distribution-free calibrated intervals, wraps any existing model
No retraining required; real coverage guarantee
Virtual Sensor Check
Estimate a parameter from correlated sensors + context
Flags sensor drift/failure vs a real engine fault
Explainability example — operator output for a lubrication alert:
"Lubrication degradation likely — driven primarily by falling oil pressure and rising oil temperature." (Oil pressure: HIGH contribution · Oil temp: HIGH · Vibration: MEDIUM · RPM: LOW)
Decision rule: AI provides decision support — not sole safety authority. Low-confidence outputs route to operator review, never blind automation.
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 10

## Slide 11
10 · STORAGE, REPLAY & OPERATOR DASHBOARD
Turning History Into a Story Engineers Can Act On
Not just raw data — a fault timeline, session comparison, and a one-page report, in minutes.
PostgreSQL Schema
Telemetry (raw/normalized)
Missions & engine information
Alerts & fault events
Health history (index, anomaly score, RUL)
Both raw and processed results stored, so engineers can investigate after a mission
Mission Replay
Fault Timeline — every alert scrubbable, with timestamp and flight phase
Session Comparison — this flight vs past flights / fleet baseline
Root-Cause Context — auto-tagged with what was happening (e.g. 'misfire during rapid throttle at high altitude')
One-Page Report — exportable PDF for the logbook
Operator Dashboard
Live values: RPM, EGT, CHT, oil P/T, fuel flow, vibration, battery
Health: index, anomaly score, predicted fault, confidence, RUL
Trends: parameter history, health trend, alert timeline
Connection status: CONNECTED / STALE / DISCONNECTED
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 11

## Slide 12
11 · VALIDATION & TEST PLAN
How We Prove the System Is Useful — Not Just Working
No accuracy claims before validation. Task-specific engineering metrics, and a pass/fail target per fault.
Fault Type | Time-to-Detect Target | False-Alarm Tolerance
Lubrication issue | Within seconds — safety-critical | Lowest — must never miss
Misfire | Within a few seconds | Very low
Combustion instability | Within a few seconds | Low
Injector abnormality | 10-30 seconds | Low
Abnormal vibration | Seconds to ~1 minute | Medium
Overheating trend | 1-3 minutes, before redline | Low — early warning is the goal
Cooling degradation | 2-5 minutes (trend-based) | Medium
Sensor drift / failure | Instant (dropout) / flights (drift) | Medium — avoid nuisance alarms
Evaluation Metrics by Module
Forecasting: MAE, RMSE
Anomaly: Precision, Recall, F1, PR-AUC
Fault diagnosis: per-fault F1, confusion matrix
RUL: MAE, RMSE, interval coverage
Real-time: inference latency, memory
Twin fidelity: state error, sync latency
Target: earlier detection than a threshold baseline, with controlled false alarms — not 99% accuracy claims.
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 12

## Slide 13
12 · COMPLETE TECHNOLOGY STACK
Every Module, Mapped to a Real Technology
Nothing here requires hardware access we don't have, or a library that doesn't exist today.
Module | Technology
Data acquisition (real path) | Sensors, ECU/FADEC, CAN, SocketCAN, python-can
Physics simulator (Member 1) | Python, NumPy — causal physics equations
Backend | Python, FastAPI, Pydantic, Uvicorn, WebSocket
State estimation | filterpy (Kalman filter)
AI/ML core | PyTorch — shared multi-task LSTM (forecast / anomaly / RUL heads)
Anomaly ensemble | scikit-learn / ruptures — CUSUM, Page-Hinkley change-point
RUL & uncertainty | Custom particle filter; MAPIE — conformal prediction
Storage | PostgreSQL (TimescaleDB later, if telemetry volume grows)
Dashboard | React + TypeScript + WebSocket + Recharts/ECharts
3D visualization (stretch) | Three.js / React Three Fiber — component-level health view
Deployment | Linux + Docker / Docker Compose
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 13

## Slide 14
13 · ACHIEVABLE BUILD ROADMAP
Phased, Not Theoretical — Every Phase Unblocks the Next
Software-only. Nothing on this roadmap requires access we don't already have.
1
Fault-Injection Simulator
Physics chain + 8 fault types + healthy-baseline validation
>
2
Real-Time Pipeline
FastAPI + WebSocket streaming, common telemetry schema, session logging
>
3
AI/ML Core
Kalman state estimation, shared multi-task LSTM, ensemble anomaly, RUL + UQ
>
4
Dashboard
Live HMI dashboard, health scores, alerts; 3D twin view as stretch goal
>
5
Mission Sim & Replay
5 environmental modes, fault timeline, session comparison, PDF report
>
6
Validation & Docs
Detection-time/false-alarm test pass, architecture docs, demo script
Every phase builds on real, working output from the previous one — nothing is a placeholder for the live demo.
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 14

## Slide 15
14 · INNOVATION CREDIT & CLOSING
Why This System Wins
Trustworthy, context-aware prognostics inside a real Digital Twin — not a dashboard with a model bolted on.
Federated Learning — Feasibility Credit
Each UAV/GCS trains locally; only model updates (never raw telemetry) sync to a fleet-wide model
Industry benchmark: ~32% fewer unscheduled engine removals reported using federated predictive-maintenance within 18 months
Honest caveat: feasibility-level for this hackathon, not a built feature
Edge AI Angle
Compact model runs onboard for instant alerts, even with no ground link
Heavier RUL/trend and fleet-learning models run on the ground server
Directly answers the PS's 'lightweight onboard analytics' innovation area
What makes this competitive:
- Context-aware (altitude + throttle + ambient + mission phase)
- Physics + AI fusion, not a black box
- Predictive health: fault risk + trend + RUL
- Sensor self-check via virtual-sensor residuals
- Explainable + uncertainty-aware outputs
- Edge-ready, fleet-scalable architecture
SIH26054 · UNIFIED ARCHITECTURE
SIH26054 · UNIFIED ARCHITECTURE — 15